## Slide 1: Madrid 13 December 2019

## Slide 2: ¿Qué es eso de cuantizar modelos?
Alexander Gonzalez
AI Software Engineer – Plain Concepts
Madrid
@alexndrglez

## Slide 4: AGENDA

## Slide 5
¿Que es la Cuantización?
  Tensorflow Lite (Post-training quantization
  Quantization-aware training
  Model Optimization
  Requisitos TF Lite
Coral Dev Board
  Dev Board and Accelerator
  MDT Flash
  Características
  ¿Que es TPU?

## Slide 6
Demo 1
  Glyphs Paper Dataset
  Mobilenet V2
  Training/Test
  Conversión TFLite
  Compilación Edge TPU
  Inferencia Coral Dev Board TPU Runtime
Demo 2
  CI/CD Raspberry Pi (IoT Edge)

## Slide 7: Why do we care?

## Slide 8: How it works?

## Slide 9
TensorFlow Lite is TensorFlow’s lightweight solution for mobile and embedded devices.
It lets you run machine-learned models on mobile devices with low latency, so you can take advantage of them to do classification, regression or anything else you might want without necessarily incurring a round trip to a server.

## Slide 10: Model Optimization
Quantizing deep neural networks uses techniques that allow for reduced precision representations of weights and, optionally, activations for both storage and computation. Quantization provides several benefits:
  Support on existing CPU platforms.
  Quantization of activations reduces memory access costs for reading and storing intermediate activations.
TensorFlow Lite provides several levels of support for quantization:
  TensorFlow Lite post-training quantization quantizes weights and activations post training easily.
  Quantization-aware training allows for training of networks that can be quantized with minimal accuracy drop, this is only available for a subset of convolutional neural network architectures.

## Slide 11: Post-training quantization
Quantizing weights
Full integer quantization of weights and activations
https://www.tensorflow.org/lite/performance/quantization_spec
Model accuracy
  It is important to check the accuracy of the quantized model to verify that any degradation in accuracy is within acceptable limits. If the accuracy drop is too high, consider using quantization aware training

## Slide 12: Quantization-aware training - Generating fully-quantized models

## Slide 13: Model requirements
Tensor parameters are quantized (8-bit fixed-point numbers)
  You must use quantization-aware training (post-training quantization is not supported).
Tensor sizes
  They are constant at compile-time (no dynamic sizes)
Model parameters
  Such as bias tensors are constant at compile-time
Tensors are either 1-, 2-, or 3-dimensional
  If a tensor has more than 3 dimensions, then only the 3 innermost dimensions may have a size greater than 1.
The model uses only the operations supported by the Edge TPU
  Logistic, Relu, Tanh, AveragePool2d…etc

## Slide 14
Glyph Detector
Discover the ancients secrets

## Slide 15
In this first development flow, we will have as main tasks, obtaining a dataset such as the Gardiner List. Then the preprocessing of the images of the data set. Extraction of characteristics of the preprocessed images and finally the corresponding training, testing and evaluation.
Preprocessing images with resize, crops, ligthning analysis, blur or smootthing…etc
Preprocess Images
With Keras and tensorflow network we extract the features of the preprocesed images and get the correspont labels for each one to package them for the training phase
Extract features
Features & training flow
Gardiner List of Egypts Glyphs
Dataset
Training, testing and evaluation

## Slide 16: Dataset

## Slide 17
TPU Compiler
Glyphs Dataset

## Slide 18: Mobilenet V1 Quantized

## Slide 20: Coral Dev Board

## Slide 21: Features
Edge TPU System-on-Module (SoM)
  NXP i.MX 8M SoC (Quad-core Cortex-A53, plus Cortex-M4F)
  Google Edge TPU ML accelerator coprocessor
  Cryptographic coprocessor
  Wi-Fi 2x2 MIMO (802.11b/g/n/ac 2.4/5GHz)
  Bluetooth 4.1
  8GB eMMC
  1GB LPDDR4
USB connections
  USB Type-C power port (5V DC)
  USB 3.0 Type-C OTG port
  USB 3.0 Type-A host port
  USB 2.0 Micro-B serial console port
Audio connections
  3.5mm audio jack (CTIA compliant)
  Digital PDM microphone (x2)
  2.54mm 4-pin terminal for stereo speakers
Video connections
  HDMI 2.0a (full size)
  39-pin FFC connector for MIPI DSI display (4-lane)
  24-pin FFC connector for MIPI CSI-2 camera (4-lane)
MicroSD card slot
Gigabit Ethernet port
40-pin GPIO expansion header
Supports Mendel Linux (derivative of Debian)

## Slide 22: MDT (Mendel Development Tool)
Mendel Development Tool (mdt)
Is a command-line tool that lets you communicate with a device running Mendel Linux
The ”mdt” command facilitates a variety of device actions such as opening a shell, installing Debian packages, pushing and pulling files, and more.

## Slide 23: TensorFlow models on the Edge TPU
What is TPU?
  Tensor Preprocessor Unit
What is Edge TPU?
  Google chip designed to run machine learning (ML) models for edge computing. Google Cloud bring us the possibility to use it.
  The Edge TPU can execute deep feed-forward neural networks such as convolutional neural networks (CNN).
  It supports only TensorFlow Lite models that are fully 8-bit quantized and then compiled specifically for the Edge TPU.

## Slide 24: TensorFlow models on the Edge TPU

## Slide 26: TPU COMPILER

## Slide 28
CI/CD Raspberry Pi

## Slide 29: CI/CD

## Slide 30: Madrid 13 December 2019